## Slide 1: Steep Turn

## Slide 2: Housekeeping
60 minutes
Emergency exit, toilet, kitchen

## Slide 3: Aim
  The aim of this briefing is to teach the student techniques used to fly level and descending steep turns using 45 and 60 angle of bank.

## Slide 4: Motivation
  Steep turns is an exercise which is intended to improve your co-ordination and competency in handling an aeroplane at a steeper angles of bank.
  Additionally, it will improve your confidence and be a benefit should the need to take evasive action arise.

## Slide 5: Overview
Objectives
Revision
Definitions
Forces acting in a steep turn
Types of steep turns
Considerations
Application
Airmanship & TEM
Summary
Objectives – revisited

## Slide 6: Objectives
At the end of the briefing, you will be able to, from memory and without mistake:
      State the relationship between lift and drag forces in a steep turn.
      State the effect of increasing the angle of bank on load factor and stall speed.
      What is the reason for adding power as the aeroplane passes through 30 angle of bank if we wish to conduct a steep level turn.
      Describe the procedure used to enter, maintain and exit from a 60 steep turn.

## Slide 7: Revision
What the effect would be on the stall speed with an increase in angle of bank.
Explain the forces acting in a medium level turn.

## Slide 8: Definitions
Bank angle
    The angle between an aeroplane’s lateral axis and the horizon.
Load factor
    The ratio of lift to the weight of an aeroplane. The units in which load factor is expressed as is “g” i.e. G force.

## Slide 9: Definitions
Rate of turn
    The number of degrees of change per second.
Radius of turn
    The distance between the aeroplane and the centre of the turn.

## Slide 10: Forces acting in a steep turn
L
W

## Slide 11: Forces acting in a steep turn
W
L
Vertical component Lift
Horizontal component lift
30°

## Slide 12: Forces acting in a steep turn
W
L
Vertical component Lift
Horizontal component lift
60°(Steep turn >30°)
Lift = 2 x Weight

## Slide 13: Forces acting in a steep turn
  At 45 AoB the induced drag is increased by 100%
  At 60 AoB the induced drag is increased by 300%
  Need to use power to counteract the increase in drag.

## Slide 14: Types of steep turns
Level steep turns
    45 and 60 AoB (power to control airspeed)
Descending steep turns
    45 and 60 AoB (airspeed is determined by AoB)

## Slide 15: Considerations
Load Factor
          Normal stall speed is 50 KIAS in clean configuration, the stalling speed IAS in a 60 AoB level turn, which has a normal ‘g’ load of 2, will be:
          50 = 50 1.414 = 70 KIAS

## Slide 16: Considerations
Stall margin
  The power is increased to combat the increased drag to maintain a margin over the stall speed. This can be referred to as a power sandwich.

## Slide 17: Considerations
Structural limitation
    PA-28 approved in both normal(+3.8, -0.0) and utility(+4.4, -0.0) categories.
    Must know structural limits as we can overstress the airframe by exceeding the maximum allowable load factor.
Notes: As we increase AoB, we increase lift & increase load factor

## Slide 18: Considerations
Physiological effects
    During steep turns the effort required by your heart to pump your blood to your brain increases as the load factor or apparent weight increases.
    The heart pumps faster when the brain senses a decrease in oxygen levels, however there is a time delay and you may experience grey/black out or even GLOC.

## Slide 19: Considerations
      Grey-out
          Usually begins with peripheral vision turning grey (tunnel vision)
          The pilot is fully conscious and still able to fly the aeroplane
          This normally occurs above 3.5g
      Black-out
          Field of view turns black
          The pilot cannot see however remains conscious
          This normally occurs above 5g (higher than limit load factor for aeroplane)
      GLOC (G-induced Loss Of Consciousness)
          Occurs at higher G loading (7g) and results in the pilot losing consciousness
          It is possible to have decreased tolerance to G loadings if the pilot had heat stress, hypoxia, low blood sugar levels

## Slide 20: Application
45 steep turn

## Slide 21: Application
60 steep turn

## Slide 22: Application
Spiral dive
  May occur if a steep turn is executed incorrectly (i.e. insufficient back-pressure or over-banking)
  Symptoms:
    Low nose attitude
    High and increasing airspeed
    High and increasing rate of turn
    High and increasing G-force

## Slide 23: Application
Spiral dive recovery
  Throttle idle
  Roll wings level and balance with rudder
  Gently ease out of dive
  As IAS reduces and nose passes through the horizon, add full power and climb at Vy

## Slide 24: Airmanship
  Lookout
  ALAP throughout the turn
  Smooth but firm control input

## Slide 25: Threat and error management
Threat | Error | Management | UAS
Traffic | Poor lookout and Situational awareness | Good lookout ALAP | 
High G manoeuvre | Insufficient speed on entry |  | Stall
Air proximity event
Maintain speed
Use power

## Slide 26: Summary
  Forces acting in a steep turn
  Structural limitations and physiological effects
  Steep turn and spiral dive

## Slide 27: Objectives – revisited
      State the relationship between lift and drag forces in a steep turn.
      State the effect of increasing the angle of bank on load factor and stall speed.
      What is the reason for adding power as the aeroplane passes through 30° angle of bank if we wish to conduct a steep level turn.
      Describe the procedure used to enter, maintain and exit from a 60° steep turn.

## Slide 28: The End